## Slide 1: Selective Parity Protection for Resilient Low-Voltage SRAM in Quantized Neural Networks
Oğulcan Aşık, Ji Wu, Kazuteru Namba
Chiba University

## Slide 2: Motivation
Large AI Models
Problem 1: High Energy Requirement
Problem 2: High Accuracy Requirement
  Need to Balance Both
What can we do about this?

## Slide 3: Common Solutions
Quantization
  Impact on Accuracy Depends on Method Used
Lowering Operating Voltage
  Increases Bit Error Rate (BER) Which Lowers Accuracy
Smaller Models
  Not Acceptable in Many Use Cases
Mixed-Precision Training
  Very Effective Reduction of Precision in Steps Where Higher Precision is not Needed
Sparse Models
  Activating Only Certain Areas in a Model Depending on the Query
Hardware Advancements like CIM
  RAM That Can Perform Certain Computations In-Memory Saving Expensive Data Transfers

## Slide 4: Methodology
ECC + Quantized Models = Lower Operating Voltage
Core Idea:
  Train CNN With 32-Bit Weight
    Quantize Weights to 4-Bit, 8-Bit & 16-Bit
  Apply Error Correcting Code (ECC) to SRAM with Low Operating Voltage
  Low Operating Voltage = Higher Bit Error Rate
  Use ECC to Correct up to 1 Bit Error in Every Model Weight
Two Methods:
  Split Bit Ranges in a Word to protected (BER = 10-4) and unprotected (variable BER)
  Same BER throughout the entire Word

## Slide 5: Methodology
32-bit
MSB LSB
8-bit
4-bit
16-bit
Hamming Code
use Hamming Code to protect LSB
16-bit
8-bit
4-bit
Quantize
No Splitting of bits
Number of Parity depends on the number of protected bits:
1-4 data bits require 3 parity bits,
5-11 data bits require 4 parity bits
12-16 data bits require 5 parity bits
use Hamming Code to protect all bits

## Slide 6: Methodology: CNN
LeNet5
Trained on MNIST dataset
number of steps: 2000
batch size: 500
Originally 32-bit weights
Conv
ReLU
MaxPool
Conv
ReLU
MaxPool
Conv
ReLU
FC
FC
ReLU
SoftMax
Input
Output

## Slide 7: Methodology: Quantization
3 Quantizations of the Weights:
  16-Bit
  8-Bit
  4-Bit
Edited Image from J. Wu and K. Namba, “Sram-based efficiency memory model for quantized convolutional neural networks,” in 2023 International Conference on Consumer Electronics - Taiwan (ICCE-Taiwan), 2023, pp. 499–500.

## Slide 8
4-bit Example:
Set parity to 1 if odd:
1 | 2 | 3 | 4 | 5 | 6 | 7
Parity 1 | Parity 2 | Data 1 | Parity 4 | Data 2 | Data 3 | Data 4
0 | 1 | 1 | 1 | 1 |  | 0
Methodology: ECC – Hamming Code Correction
P1 1 1 0 => P1 = 0
P4 1 0 0 => P4 = 1
P2 1 0 0 => P2 = 1

## Slide 9: Methodology: ECC – Hamming Code Correction
4-bit Example:
Check if even:
1 | 2 | 3 | 4 | 5 | 6 | 7
Parity 1 | Parity 2 | Data 1 | Parity 4 | Data 2 | Data 3 | Data 4
0 | 1 | 1 | 1 | 1 | 1 | 0
Error
P4: 1 1 1 0 is odd => Error! Position found!
P1: 0 1 1 0 is even => OK
P2: 1 1 1 0 is odd => Error!
=> Error Position = 2 + 4

## Slide 10: Methodology: Bit Error Simulation
Convert Model Weights to Bit Arrays
Generate Random Bit Mask According to The Resulting Size and BER
Flip Bits Using Bit Mask
Convert Bit Array Back into Model
[
]
[
[
[
]
]
]
[
]
[
]
[
]
[
]
[
]
[
]
[
]
[
]
[
]
[
]
1. Convert data
[
]
[
]
[
]
[
]
[
]
[
]
[
]
[
]
[
]
[
]
3. Flip Bits
Weights
In Model
2. Generate Random Bit Flip Mask
Weights as Bit Array
4. Convert Back

## Slide 11: Results: 8-Bit with Split BERs
ECC allows increasing the BER up to 0.025 with minimal accuracy cost
8-bit Quantization [0,1) protected
BER
Accuracy
8-bit Quantization [0,6) protected
Accuracy
BER
[0,1) indicates that bit 0 only is protected, with [0,6) it is 0, 1... 5

## Slide 12: Results: 8-Bit with Split BERs

## Slide 13
Results: 4-Bit with Split BERs
ECC allows increasing the BER up to 0.05 with minimal accuracy cost
4-bit Quantization [0,1) protected
4-bit Quantization [0,2) protected
BER
Accuracy
BER
Accuracy

## Slide 14: Results: 16-Bit with Same BERs
Accuracy worsened by ECC
BER up to 0.003
16-bit Quantization No Protected Bits
16-bit Quantization No Protected Bits
Accuracy
Accuracy
BER
BER

## Slide 15: Results: 8-Bit with Same BERs
ECC allows increasing the BER up to 0.025 with minimal accuracy cost
BER
8-bit Quantization No Protected Bits
Accuracy

## Slide 16: Results: 4-Bit with Same BERs
ECC allows increasing the BER up to 0.05 with minimal accuracy cost
BER
4-bit Quantization No Protected Bits
Accuracy

## Slide 17: Results: Potential Energy Saving1
Split BER:
Same BER:
L. Yang and B. Murmann, "SRAM voltage scaling for energy-efficient convolutional neural networks," 2017 18th International Symposium on Quality Electronic Design (ISQED), Santa Clara, CA, USA, 2017, pp. 7-12, doi: 10.1109/ISQED.2017.7918284.1
 | Unprotected | 8-Bit | 4-Bit
Voltage | 0.54V | 0.49V | 0.47V
BER | 10-4 | 0.025 | 0.05
 | 16-Bit (no ECC) | 8-Bit | 4-Bit
Voltage | 0.51V | 0.49V | 0.47V
BER | 0.003 | 0.025 | 0.05

## Slide 18: Conclusion
ECC allows higher BERs without sacrificing model accuracy
Cost and Effort of Splitting up Operating Voltages is not worth it
Most effective Energy Saving via low bit count combined with ECC method
ECC + Quantization makes Energy Saving without significant Accuracy loss possible

## Slide 19: Thank You For Listening